## Slide 1
Altamash Asif Ghori
and
Afnan
Organic Presentation

## Slide 2
Glycerol
+
Long chain fatty acids
Long chain fatty
acid ester
+
water
Oil manufacturing

## Slide 3
Method applied for
the extraction of Oil
1.Rendering
2.Mechanical press
3.Solvent Extraction

## Slide 4
NON-GLYCERIDIC CONSTITUENTS in OILS
Free Fatty acids
Partial Glycerides ( mono- or di- glyerides)
Phosphatides
Sterols
Hydro carbons
Pigments (gossypol, chlorophyll)
vitamins(carotene)
Sterols glucosides
Protein fragments
Traces of pesticides
Heavy metals

## Slide 5
Methods for the refining of oils
Two main refining routes are
alkaline refining and
physical refining (steam stripping,
distillative neutralisation )
which are used for removing the free fatty acids.

## Slide 6
STEPS OF REFINING OF OILS
Degumming
Neutralization
Bleaching
Deodorizing
Winterizaton
hydrogenation

## Slide 7
Degumming
Addition of water ( 2 to 3%) to
precipitate out phosphatides
Using an acid such as citric, malic
or phosphoric acid and water
Using an acid and sodium hydroxide
Purpose: to remove phosphatides contents.

## Slide 8
NEUTRALIZATION
Purpose: Treated with strong base to neutralize free fatty acids
and additional acid contents in it with partial glycerides.
Naoh or with phosphoric acid and naoh
Koh
Ca(oh)2
Nh4oh
Lithium hydroxide etc….

## Slide 9
BLEACHING
fUller’s earth
Bentonite Clay
amorphous silica
Purpose: sterols, Hydro carbons, pigments,
traces of pesticides and sterol glucosides.

## Slide 10
winterization
Example: Palm oil
Stearin (solid fat)
And olein (liquid oil)

## Slide 11
deodorization
Bubbling of steam ( sparging )
Charcoal
Purpose: odor is removed
138 to 800 pa of vacuum
210 t0 275 degree centigrade

## Slide 12
Hydrogenation
Oil + H 2
fats
Catalyst : nickel, palladium or platinum
Purpose: to convert oil into fat so it wont get oxidize
Or its peroxide value not increase.
200 to 700 kpa gauge
140 to 250 degree centigrade temperature
190 is most common temperature
Catalyst reacts at 150 degree centigrade

## Slide 13
Agitation: 75 to 150 rpm
Cool at 20 degree centigrade
Hydrogen pressure 40 to 60 psig
Time 40 to 60 minutes

## Slide 14
finished