## Slide 1
Chapter # 7
Sulfonation
and
Sulfation

## Slide 2
Sulfonating agents.

## Slide 3
Sulfonation:-
Sulfonation may be defined as any chemical process by which the sulfonic acid group ( -SO2OH) ,the corresponding salts, SO3 , SO2 or the sulfonyl halide group (-SO2Cl) is introduced into an organic compound.
These groups may be situated on either a carbon atom or nitrogen atom
Sulfation:-
Sulfation is when SO3,SO3H,SO2 is directly bond with oxygen is called Sulfation.
R-H + H-HSO4 R-HSO3 + H2O
R-H + SO3 R-SO3H
R-OH + SO3 R-O-SO3H
Sulphonic Acid
(Sulphonic Acid)
(Sulfonicperacid)

## Slide 4
NH3 + SO3
Sulfamation:-
Sulfamation is when SO3,SO2,HSO3 directly bounded with Nitrogen.
HO-S-NH2
O
II
II
O
(Sulfamic acid)

## Slide 5
Sulphonating agents and Sulfating agents.
These agents may be sumerized as follows:
1.Sulfur Trioxide and Compounds thereof.
a.Sulfur Trioxide,Oleum,Concentrated Sulfuric Acid.(SO2 + H2O)
b.Chlorosulfonic Acid.(SO2+HCL)
c.Sulfur Trixode adducts with organic compound.
d.Sulfamic Acid.

## Slide 6
SO3:
SO3 is an aggressive electrophilic reagent that rapidly reacts with any organic compound containing an electron donor group.
Sulfonation is difficult reaction to perform on industrial scale because the reaction is highly exothermic and so rapid releasing 380 KJ/Kg SO3 reacted.
Most organic compounds forms a black char on contact with pure SO3 due to rapid reaction and heat evolution.
Liquid SO3:
It gives fast reaction with organic compounds . The disadvantage is that we cannot control the reactivity because SO3 ion liquid state is extremely reactive . But the problem of SO3 has been solved by diluting the SO3 to moderate the reaction.
HCI + SO3
H-O-S-Cl (Chlorosulfonic acid)
O
II
II
O
H20+SO3
H2SO4+SO3
H2S2O7 (Oleum)

## Slide 7
Gaseous SO3
Properties are same as liquid SO3.
Dry air + SO3
2.5% to 8% SO3 in Dry Air

## Slide 8
Sulfuric acid (Conc.) and Oleum:
Conc. Sulfuric Acid and Oleum are widely used as sulfonating agents. Oleum is used to sulfonate alkyl benzene and sulfate fatty alcohol for heavy duty detergents.
It is an equilibrium process , as water is formed in this reaction and resultant water dilutes the Oleum / Sulfuric acid. The sulfonation reaction stops when the sulfuric acid concentration drops to 90%.
This spent acid may be separated from alkyl benzene sulfonic acid to produce product which on neutralization contains a relatively low level 6 to 10% of sodium sulfate.
When fatty alcohols are sulfated the spent acid cannot be separated . It must be neutralized with alcohol sulfuric acid to make product containing a high level of sodium sulfate.
H - O - S - O – H +
O
II
II
O
(CH2)11-CH3
H+ O- -S- -(CH2)11-CH3 + H2O
O
II
II
O
Alky Benzene
Alkyl Benzene sulfonic acid

## Slide 9
Oleum contains 90% SO3 and 10% H2SO4.
Sulfonation by Oleum:
+ H2S2O7
H2SO4 in excess
SO3H
+ H2O

## Slide 10
Chlorosulfonic acid:
Cl-HSO3 is widely used to prepare alcohols sulfate,dyes and dye intermediates.
Note that as the reaction moves to completion,HCl is released.This acid must be scrubbing or other wise scrubbed.Because HCl is a corrosive substance if we are going to use this sulfonating agent so reactor must be made of stainless steel or line with steel to avoid corrosion.Moreover this agent is expensive source of SO3.
H-O-S-Cl + CH3-(CH2)10-CH2-OH
O
II
II
O
Lauryl Alcohol
CH3-(CH2)10-CH2-O-S-O-H+ + HCL
O
II
II
O
Alkyl benzene sulfonic acid

## Slide 11
Sulfur Trioxide adducts from Organic compound:
Sulfur trioxide usually obtained from rotten eggs.

## Slide 12
Sulfamic Acid:
Sulfamic acid is used to sulfate alcohols and ethoxylated alcohols to form ammonium nutralized salts.The reaction goes directly to the ammonium salt of the alcohol sulfuric acid.But its an expensive source of SO3.
CH3-(CH2)8- -(O-CH2-CH2)4-OH + NH2SO3H
Alkyl phenol ethoxylated
Sulfamic acid
CH3-(CH2)8- --(O-CH2-CH2)4-O-S-O+ NH4-
O
II
II
O
Alkyl phenol ethoxylated ammonium sulfate
Its advantage is it doesn’t effect aromatic ring but only bond with sulfate alcohols.

## Slide 13
The sulfur dioxide and compounds thereof.
SO2 is so reactive so we dilute it with gases to decrease its reactivity.
a.Sulfur Dioxide with with Chlorine.
b.Sulfurous acid,metallic sulfides.
c.Sulfur dioxide with oxygen:
SO2+CL2+R-H
RSO2CL+HCL
R-H+SO2+O2
R-SO2-O + Acid
CHLOROSULFONIC ACID

## Slide 14
Sulfuric Acid(H2SO4) | Sulfur Trioxide(SO3)
Slightly Exothermic(Slow). | Highly Exothermic(Fast).
Partially Complete . | Complete.
Yes. | No.
Minimum. | Maximum.
Large(need continuous batch). | Very small.
Easily. | In liquid form.
Rate of Reaction
Extent
Spent Acid
By Product
Reactor Size
Availability
Gases reactor are very small because gases are compressible.
Oleum properties are between Sulfuric acid and Sulfur Trioxide.
Difference in Sulfuric acid and sulfur trioxide.